## Slide 1: The effects of Impeller Size and Speed on Fluid Mixing
Experiment 10 – team ten
Bo Bramer, Clark Wey, Jose Leal, Angel Rodriquez

## Slide 2: Topics Covered
Introduction (background, ethics, objectives)
Materials and Methods
Theory
Results
Discussion
Conclusion

## Slide 3: Introduction – Background
Common in industrial applications
  Oil and gas industry
  Food industry
Convert heterogeneous to homogeneous
  Single or multiphase
  One or many components

## Slide 4: Introduction – Background
Difficult process
  Every system has different design variables
No “one-size-fits-all” mixing system
Important to know how any variable affects the mixing process

## Slide 5: Introduction – Ethics
Important to have thorough mixing
  Increased cost, increased time
When not mixed thoroughly, problems arise
  Endanger both environment and process
AIChE code of ethics
  “hold paramount the safety, health and welfare of the public and protect the environment in performance of their professional duties”

## Slide 6: Introduction – Ethics
Thermal Runaway
  Catastrophic effect on environment and process
    Destroying environment
    Low product yield
Dec 19th, 2007
  T2 Laboratories in Florida
  4 deaths, 32 injuries

## Slide 7: Introduction – Objectives
Know how different variables affect mixing process
  Density, components, mixing speed, etc.
Characterize mixing in acrylic tank of water with different variables
  Blade size, mixing speed, presence of baffles

## Slide 8: Materials and Methods
Different sized impeller blades
  2.1x6.2, 4.3x6.2, 6.5x6.2 cm
  Different widths, same lengths
Different impeller speeds
  150, 250, 350 RPM
Conductivity probe to determine mixing time
Force meter to determine torque on motor

## Slide 9: Theory
Reynolds number
Power number
Froude number
: Fluid density
: Impeller rotational speed
: Impeller Diameter
: Fluid dynamic viscosity
: Mixing power
: Gravitational acceleration

## Slide 10: Theory
Blending time number
: blending time

## Slide 11: Theory
Expected Reynolds number vs. mixing time number plots

## Slide 12: Theory
Expected Reynolds number vs. power number plot

## Slide 13: Results
Blade width vs. time to mix while holding rotation speed constant shows negative correlation

## Slide 14: Results
Rotation speed vs. time to mix while holding blade width constant shows no significant correlation

## Slide 15: Results
Reynolds number vs. blending time number shows weakly negative correlation

## Slide 16: Results
Reynolds number vs. power number shows that over increasing Reynolds number, increase in blade width to blade length ratio led to decrease in power number

## Slide 17: Discussion
Increasing blade width decreased time to mix
Increasing blade speed did not decrease time to mix
Increasing Reynolds number had a weakly negative correlation with blending time number
Increasing Reynolds number led to a decrease in power number

## Slide 18: Discussion
Reynolds number vs. blending time number

## Slide 19: Discussion
Reynolds number vs. power number

## Slide 20: Conclusion
Increasing blade widths significantly decreased mixing time
Increasing impeller speeds did not
Higher Reynolds numbers lead to better performance
  Mixing time number, power number

## Slide 21: Conclusion
Approach for scaling up
  Holding power number constant
Future steps
  Changing angles of blades
  Expect angles closer to vertical to have lower blending time but higher power number

## Slide 22: Citations
J. B. McClintock, R. A. Angus, M. R. Mcdonald, C. D. Amsler, S. A. Catledge, and Y. K. Vohra, ``Rapid dissolution of shells of weakly calcified Antarctic Benthic macroorganisms indicates high vulnerability to ocean acidification: Antarctic Science,'' Cambridge Core, 01-Oct-2009. [Online]. Available: https://www.cambridge.org/core/journals/antarctic-science/article/abs/rapid-dissolution-of-shells-of-weakly-calcified-antarctic-benthic-macroorganisms-indicates-high-vulnerability-to-ocean-acidification/DC9B2354DAACA88BC5305C1D69BB578D. [Accessed: 19-Oct-2021].
“Code of Ethics.” AIChE's, 21 Aug. 2020, https://www.aiche.org/about/governance/policies/code-ethics.
“T2 Laboratories Inc.. Reactive Chemical Explosion.” CSB, https://www.csb.gov/t2-laboratories-inc-reactive-chemical-explosion/.
Kummer, Alex, and Tamás Varga. “What Do We Know Already about Reactor Runaway? - A Review.” Process Safety and Environmental Protection, vol. 147, 2021, pp. 460–476.